## Slide 1: IP Mobility Overview

## Slide 2: Classification of Mobility (by Movement Type)
L1 Mobility
L2 Mobility
L3 Mobility
Vertical Handover & Roaming

## Slide 3: L1: Movement within a Base Station
Same MAC address
Same IP address
BS
MN
Physical Layer MM (by 주파수 강도 제어)

## Slide 4: L2: Movement across different BS
Different MAC address
Same IP address
BS1
MN
BS2
Router
Internet
MAC Layer MM

## Slide 5: L3: Movement across different IP subnets
Different MAC address
Different IP address
BS1
MN
BS2
R_1
Internet
R_2
Network Layer MM (IP Mobility)

## Slide 6: Vertical Handover
MN
3G Cellular
Movement across different radio access technology
MN has multiple network interfaces (e.g., WiBro & 3G)
WiBro …

## Slide 7: Roaming between Operators
MN
SKT
Roaming between different operators
AAA interworking: AAA proxy (visited)  AAA home
LGT

## Slide 8: Mobility Management
Two Technical Issues
  Location Management (위치관리)
    Maintains the current location of mobile users
      Location: BS or IP address ?
    For up-coming sessions
    (e.g.) Binding Update
  Handover Control (핸드오버 제어)
    Provides ‘Session Continuity’ against movement of MN
    For on-going sessions
    (e.g.) Handover Tunnel

## Slide 9: Handover
Vertical & Horizontal Handover
  Vertical Handover
    Handover across heterogeneous access networks
    (e.g.) 3G-WiBro
    MN has multiple network interfaces
  Horizontal Handover
    Handover between homogeneous access networks
    3G-3G: different IP subnet (IP address changes)
    MN has a single network interface

## Slide 10: Handover
L2 & L3 Handover
  L2 Handover (link-layer HO)
    PoA (Point of Attachment) of MN changes
    Typical L2 handover delay (link switching delay) = 200 ms
  L3 Handover (IP Handover)
    IP address of MN changes
      (e.g.) IP subnet change
      DHCP or IPv6 address configuration
    Typical L3 handover delay = several seconds

## Slide 11: Mobile IP (MIP)
IETF

## Slide 12: Classification of Mobile IP
Mobile IPv4 (MIPv4)
  MIPv4
  Low-Latency Handover for MIPv4 (FMIPv4)
  Regional Registration for MIPv4 (HMIPv4)
Mobile IPv6 (MIPv6)
  MIPv6
  Fast Handover for MIPv6 (FMIPv6)
  Hierarchical MIPv6 (HMIPv6)

## Slide 13: MIPv4: Overview
MIPv4 Nodes
  MN (Mobile Node): Host
  CN (Correspondent Node): Host
  HA (Home Agent): Router
  FA (Foreign Agent): Router
MIPv4 IP address
  HoA (Home Address): MN
  CoA (Care-of-Address): FA

## Slide 14: MIPv4: Data Flows

## Slide 15: MIPv4: Control Operations
Movement Detection
  MN  FA (CoA)
  ICMP Agent Solicitation & Advertisement
Registration to HA (via FA)
  MN  FA  HA
  Over UDP (destination port 434)
Data Tunneling
  CN => HA (HoA) => FA (CoA) => MN
  IP-in-IP Tunneling, ..

## Slide 16: MIPv4: Control & Data Flows

## Slide 17: MIPv4: Tunneling Schemes

## Slide 18: MIPv4: IP-in-IP Tunneling

## Slide 19: MIPv4: Triangular Routing Problem

## Slide 20: MIPv4: Reverse Tunneling

## Slide 21: MIPv4: Binding Update
Route Optimization !

## Slide 22: Mobile IPv6 (MIPv6)
MIPv6 = MIPv4 + IPv6
  IPv6 특성에 맞게 MIPv4를 변경
Major Differences from MIPv4
  FA의 기능이 MN 내부로 포함됨 (FA가 없음)
    MIPv6 Nodes: MN, CN, HA
  CoA: MN의 IP 주소 (MIPv4 CCoA와 유사)
    By DHCPv6 or IPv6 Stateless Auto-Configuration
  Binding Update (BU): MN  HA or CN
    Mobility Header (a new IPv6 extension header)
    Intrinsic Route Optimization
    MIPv6 is in the base IPv6 protocol

## Slide 23: MIPv6: Basic Operations

## Slide 24: MIPv6: Basic Operations

## Slide 25: MIPv6: Binding Update

## Slide 26: MIPv6: Changes to IPv6
New IPv6 Protocol (Header)
  Mobility Header
    A new IPv6 extension header
  New Option in Destination Option Header
    Home Address Option
  New Type in Routing Header
    Type 2 Routing Header
New ICMP Messages
  ICMP HA Address Discovery Request/Reply
  ICMP Mobile Prefix Solicitation/ Advertisement

## Slide 27: MIPv6: Mobility Header
A new IPv6 extension header
  Home Test Init Message
  Care-of Test Init Message
  Home Test Message
  Care-of Test Message
  Binding Update Message
  Binding Acknowledgement Message
  Binding Error Message
  Binding Refresh Request Message

## Slide 28: MIPv6 Extensions
Mobile IPv6 (MIPv6)
  Fast Handover for MIPv6 (FMIPv6)
  Hierarchical MIPv6 (HMIPv6)

## Slide 29: FMIPv6: Reference Architecture
MN
PAR
NAR
CN
Trigger

## Slide 30: FMIPv6: Operations
Handover Initiation
  L2 Triggers, RtSolPr, PrRtAdv
    Between MN and AR
Tunnel Establishment
  To reduce the packet losses during handover
  HI (Handover Initiate) and HACK
    Between PAR and NAR
Packet Forwarding
  PAR => NAR (data buffering at NAR):FBU, FBack
  NAR => MN: FNA (Fast NA)

## Slide 31: FMIPv6: Operational Flows

## Slide 32: HMIPv6: Overview
HMIPv6 Nodes
  Hosts: MN, CN, HA
  Routers: AR, Mobile Anchor Point (MAP)
IP Address (CoA)
  RCoA (Regional CoA): in the MAP region
  LCoA (On-Link CoA): in the AR region

## Slide 33: HMIPv6: Architecture
HA
CN
MAP
AR1
AR2
MN
RCoA
Movement
LCoA_1
LCoA_2

## Slide 34: HMIPv6: Operations
MN
  When entering an AR region in the MAP domain,
    it gets LCoA (AR region) and RCoA (MAP region)
    RCoA does not change in the MAP domain
  Local Binding Update (LBU) to MAP
    Bind LCoA & RCoA to MAP
MAP (Acting as a local HA)
  Only the RCoA need to be registered with CN/HA
  Relay all packets between MN and HA/CN

## Slide 35: HMIPv6: MAP Tunnel (MAP  MN)
HA
CN
MAP
AR1
AR2
MN
LCoA
MAP
RCoA
CN
Home Addr
Outer header
Inner header

## Slide 36: MIP in 3GPP2

## Slide 37: MM: Recent Issues
Proxy MIPv6 (PMIPv6)
Distributed Mobility Management (DMM)

## Slide 38: Proxy Mobile IPv6 (PMIPv6)
PMIPv6
  Network-based Localized Mobility Management protocol
  IETF NETLMM WG
Motivations
  Host-based Mobile IPv4/v6 has not been yet deployed
  Why ?
    Too heavy specification of MIPv4/v6 on a small terminal
    Battery problem
    Waste of air resource

## Slide 39: PMIPv6
Host-based vs. Network-based MM
Host-based Mobility
Network-based Mobility
AR
HA
Route Update
Movement
Movement
HA
Route Update
AR

## Slide 40: PMIPv6: Overview
LMA Address
LMM (Localized Mobility Management) Domain
MAG1
Host B
Host A
LMA
Proxy Binding Update (PBU)
Control message sent out by MAG to LMA to register its correct location
Home Network MN’s Home Network
Proxy Care of Address (Proxy-CoA)
The address of MAG.
IP Tunnel
IP-in-IP tunnel LMA and MAG.
MAG2
LMA: Localized Mobility Agent MAG: Mobile Access Gateway
MN’s Home Network Prefix (MN-HNP)
CAFE:2:/64
MN’s Home Network Prefix (MN-HNP)
CAFE:1:/64
MN Home Address (MN-HoA)

## Slide 41: PMIPv6 Operations
Tunnel Setup
This can be omitted when stateless configuration is used.
MAG emulates the MN’s home link
In case that profile store does not have MN Home Prefix

## Slide 42: PMIPv6: Benefits
No host stack change for IP mobility
Avoiding tunneling overhead over the air
Re-use of Mobile IPv6
  PMIPv6 is based on Mobile IPv6 [RFC3775].

## Slide 43: Distributed Mobility Management (DMM)
Problem Statements & Requirements
DMM Approaches

## Slide 44: Centralized MM
Current cellular networks
  Hierarchical architecture
Centralized mobility anchor
  HA, LMA

## Slide 45: Distributed MM
Future mobile networks
  Flat architecture
Mobility management
  Distributed Control
  Distributed anchors: HA/LMA => AR/MAG
Advantages
  Optimal routes
  Low control overhead
  Handling a single point of failure and attack

## Slide 46: DMM Requirements (1)
DMM should be designed to consider
  Distribution of the mobility anchors (e.g. HA)
    In order to achieve a more flat design
    This would improve scalability and robustness of the mobility infrastructure
  Placing the MM closer to the edge of network (e.g. AR)
    In order to achieve routing optimality and lower delays
    Offloading near the edge of the network
    Benefit of the core network load

## Slide 47: DMM Requirements (2)
DMM should be designed to consider
  Separating control and data planes by splitting location and routing anchors
    This could minimize the signaling overhead between the mobility anchors
    We may keep the control plane centralized, with the data plane distributed
  Reusing existing protocols while minimizing changes,
    in order to allow faster adoption of the technology

## Slide 48: DMM Approaches
Partially Distributed MM
Fully Distributed MM

## Slide 49: Partially Distributed MM
Only data plane is distributed
  With centralized control plane

## Slide 50: Fully Distributed MM
Both data and control planes are distributed
  Data-driven versus Search-driven